## Slide 1: Pool Regulation Changes for 2018
David Hornsby, REHS
Area Manager

## Slide 2: Minimum Disinfectant Levels
Minimum disinfectant levels vary due to type of pool and whether using stabilizer(cyanuric acid).

## Slide 3: Spas
Minimum free chlorine level is 3.0 parts-per-million (ppm).
Minimum bromine level is 4.0 ppm.

## Slide 4: Interactive Water Play Pool (Spray Pad)
Minimum free chlorine level is 2.0 ppm.
Minimum bromine level is 3.0 ppm.

## Slide 5: Activity Pool
This includes, but is not limited to slides, flumes, lily pad walks, log rolls, cable, rope, boom drops, and any other falling entry features.
Minimum free chlorine level is 2.0 ppm.
Minimum bromine level is 3.0 ppm.

## Slide 6: Wading Pool
Minimum free chlorine level is 2.0 ppm.
Minimum bromine level is 3.0 ppm.

## Slide 7: All Other Pools
Minimum free chlorine level is 1.0 ppm unless using cyanuric acid, then the minimum level is 2.0 ppm.
Minimum bromine level is 3.0 ppm.

## Slide 8: Maximum Level of Disinfection
The maximum level of free chlorine for all pools and spas is 10.0 ppm.
The maximum level of bromine for all pools and spas is 8.0 ppm.

## Slide 9: Combined Chlorine Maximum Level
The maximum level of combined chlorine in all pools and spas is 0.4ppm.

## Slide 10: Gas Pool Heater Inspections
A third party inspection is required of gas pool heaters.

## Slide 11: Pool Signage
When applicable “No Lifeguard on Duty” sign must be a minimum of 4 inch letters.
Pool signage in clear public view must include that animals, except service animals, are not allowed in the pool enclosure.
Spas must have an additional rule posted, in clear public view, to address the maximum temperature being 104 degrees Fahrenheit.

## Slide 12: Main Drain Covers
All main drain covers must meet meet the federal anti-entrapment requirements.

## Slide 13: Main Drain Cover Approved Example
All main drains must have approved covers installed.

## Slide 14: Main Drain Cover Approved Example
Covers cannot be broken, missing or out of place.

## Slide 15: Main Drain Cover Approved Example

## Slide 16: Main Drain Covers Approved Examples

## Slide 17: Main Drain Covers Unapproved Examples

## Slide 18: Equalizer Suction Line Covers
All equalizer line openings into the pool must have an approved cover installed.

## Slide 19: Equalizer Suction Line Covers Approved Example

## Slide 20: Equalizer Suction Line Covers Approved Example

## Slide 21: Equalizer Suction Line Covers Approved Examples

## Slide 22: Equalizer Suction Line Covers Unacceptable Example

## Slide 23: Equalizer Suction Line Covers Unapproved Example

## Slide 24: Equalizer Suction Line Covers Unapproved Example

## Slide 25: Equalizer Suction Line Covers Disablement
An approved cover on the equalizer suction line is not needed if the equalizer line has been disabled.
Even if the equalizer line is disabled an unbroken cover must be in place to prevent entrapment.

## Slide 26: Equalizer Suction Line Covers Disablement
Not Disabled
Disabled

## Slide 27: Updated Imminent Health Hazards
Any violation will require closure of the pool until corrected:
Suction outlet main drain covers and skimmer equalizer line covers must meet federal anti-entrapment requirements.
a. Approved covers must be installed.
b. Covers cannot be broken, missing or out of place.
Vacuum caps must be in place.

## Slide 28: Updated Imminent Health Hazards
Any violation will require closure of the pool until corrected:
3. Disinfectant levels based on pool type:
a. Spas
* 3.0 - 10.0 ppm free chlorine
* 4.0 - 8.0 ppm bromine
b. Activity / Interactive / Wading Pools/Spray Pads
* 2.0 - 10.0 ppm free chlorine
* 3.0 - 8.0 ppm bromine
c. All Other Pools
* 1.0 - 10.0 ppm free chlorine of no cyanuric acid chlorine stabilizer used.
* 2.0 - 10.0 ppm free chlorine if cyanuric acid chlorine stabilizer is used.

## Slide 29: Updated Imminent Health Hazards
Any violation will require closure of the pool until corrected:
4. pH must be maintained between 7.2 - 7.8.
5. Filtration system/disinfection system must be functioning.
6. Main drain cover must be clearly visible in the bottom of the pool.
7. No broken glass or other sharp objects in the
pool or on the pool deck.

## Slide 30: Updated Imminent Health Hazards
Any violation will require closure of the pool until corrected:
7. Approved barrier, including self-closing, self-latching gate, must be in place.
8. All water supplying pools or pool facilities must be from an approved source. Well water must be tested to make sure it is potable.
9. Any fecal or vomit incident.

## Slide 31: QUESTIONS?
David Hornsby, REHS
Area Manager
770-963-5132, Ext. 514
david.hornsby@gnrhealth.com